## Slide 1: The Spectral Information System SPECCHIO V3.3 - Introduction
Andy Hueni1
1 Remote Sensing Laboratories, University of Zurich, Switzerland
Date: 2019-05-04

## Slide 2: Agenda
Spectral Information Systems: Raison d'être
Metadata
Methods
    SPECCHIO Architecture
    Spectroscopy Lifecycle Support
  Results

## Slide 3: Spectral Information Systems: Raison d'être
Spectral Information Systems are systems for building and providing spectral information, utilising spectral databases as repositories for spectral data and associated metadata.
Where the heck are my spectra I collected just last summer?
http://phdcomics.com

## Slide 4: Common Issues in Field Spectroscopy
Where are my data files?
http://phdcomics.com
What were the sampling context and conditions?
My instrument is not producing the truth?!?
... and there are thousands of them: how to keep track?
Can someone else make use of my data?

## Slide 5: On the Importance of Metadata
W. K. Michener, J. W. Brunt, J. J. Helly, T. B. Kirchner, and S. G. Stafford, "NONGEOSPATIAL METADATA FOR THE ECOLOGICAL SCIENCES," Ecological Applications, vol. 7, pp. 330–342, 1997.

## Slide 6: SPECCHIO Spectral Information System
Metadata = Contextual Awareness
Methods

## Slide 7: Architecture – V3
SPECCHIO Server
Glassfish Application Server
& Web Server
MySQL Database Server
User Workstation
HTTPS Port
Java VM (JRE 1.6)
SPECCHIO App
Pure Java
SPECCHIO
DB
Higher Level Languages
App
with SPECCHIO
Java
components
Port 3306
SPECCHIO API
Web Browser Interface
Relational storage of spectral data and metadata
Data sharing / Multiuser / Research Groups
Open source/access components

## Slide 8: Spectroscopy Lifecycle Support
Experimental Planning
Data Acquisition
Data
Ingestion
Metadata Augmentation
Data Processing
Information Retrieval
SPECCHIO
Spectral
Information
System
Automation, because data entry is tedious!
Add metadata to spectral data in a smart way (group updates for redundant data!)
Allow processing without data export to files. Keep provenance information.
Search by adding metadata constraints

## Slide 9: Spend your research time analysing data instead of trying to find it on your file system.
Spectral
Files
SPECCHIO Server
SPECCHIO
DB
Data ingest:
Either via SPECCHIO GUI,
or if no reader exists, use our own implementation in Matlab or R
Data Augmentation and processing: add metadata to spectra and apply spectral processing.
Meta
Files
Data Analysis: easiest in Matlab/R
Insert
Select/Insert
Data Search: SPECCHIO GUI & Matlab/R work well in concert or stand-alone
Select&Search

## Slide 10
Results
Practical Use
Installation/Availability
Experimental Planning
Data Acquisition
Data
Ingestion
Metadata Augmentation
Data Processing
Information Retrieval
SPECCHIO
Spectral
Information
System

## Slide 11: Concepts - Data Input
Intelligent
data input
process
SPECCHIO
Spectral
Database
File system
Spectral files
&
user defined structures
Spectral data
Automatically extracted metadata
Experimental Planning
Data Acquisition
Data
Ingestion
Metadata Augmentation
Data Processing
Information Retrieval
SPECCHIO
Spectral
Information
System
Notes: The first concept we are looking at is the data input.
This is a typical dataflow, where an object is sampled in the field using a spectroradiometer, generating spectral files. These spectral files are stored in user defined structures on the file system.
We then use an intelligent data input processes to read the spectral information and automatically extract metadata and insert these data into the database.

## Slide 12: Metadata Augmentation
Group updates
Conflict detection
Application domain categories
Automatic inserts:
  Altitude
  Measurement support
  Solar angles
  Goniometer Angles
Experimental Planning
Data Acquisition
Data
Ingestion
Metadata Augmentation
Data Processing
Information Retrieval
SPECCHIO
Spectral
Information
System

## Slide 13: Metadata Augmentation from XLS
  Auto-matching to existing metadata in DB
Experimental Planning
Data Acquisition
Data
Ingestion
Metadata Augmentation
Data Processing
Information Retrieval
SPECCHIO
Spectral
Information
System

## Slide 14: Even with Automation, Metadata Entry takes Time!
Standard input with majority of metadata only read from spectrometer file.
Careful data curation effort, involving manual labour

## Slide 15: Spectral Processing: Reflectance Calculation
Interactive processing: jump-corrected radiances to reflectance factors using linear irradiance estimation. Reflectance factors are inserted into the SPECCHIO database, linking with all previously entered metadata
Experimental Planning
Data Acquisition
Data
Ingestion
Metadata Augmentation
Data Processing
Information Retrieval
SPECCHIO
Spectral
Information
System

## Slide 16: Data Selection
Interactive Query Building
Metadata space restrictions
cond = EAVQueryConditionObject('eav', 'spectrum_x_eav', 'Lutein', 'double_val');
cond.setValue('0.001');
cond.setOperator('>=');
query.add_condition(cond);
cond = EAVQueryConditionObject('eav', 'spectrum_x_eav', 'Lutein', 'double_val');
cond.setValue('5.0');
cond.setOperator('<=');
query.add_condition(cond);
cond = EAVQueryConditionObject('eav', 'spectrum_x_eav', 'Violaxanthin', 'double_val');
cond.setValue('1.0');
cond.setOperator('>=');
query.add_condition(cond);
cond = EAVQueryConditionObject('eav', 'spectrum_x_eav', 'Violaxanthin', 'double_val');
cond.setValue('4.0');
cond.setOperator('<=');
query.add_condition(cond);
Autogenerated query code, for use in Matlab or R:
Experimental Planning
Data Acquisition
Data
Ingestion
Metadata Augmentation
Data Processing
Information Retrieval
SPECCHIO
Spectral
Information
System

## Slide 17: Availability and Installation: Online System
SPECCHIO Server
Glassfish Application Server
& Web Server
MySQL Database Server
HTTPS Port
SPECCHIO
DB
Port 3306
Online multiuser DB for data sharing and testing of the system.
OPTIMISE Training School data are available online
Web Interface
Java Client

## Slide 18: Availability and Installation: Desktop Client
Java
Runs on macOS, Linux, Windows, etc
GUI
Connection to any open access SPECCHIO database

## Slide 19: Availability and Installation: SPECCHIO Virtual Machine

## Slide 20: Availability and Installation: Open Source
All SPECCHIO code (client and server) is open source and can be found on GitHub: https://github.com/SPECCHIODB/SPECCHIO

## Slide 21: Thank you for your attention!
For more information on the current version of SPECCHIO see: www.specchio.ch
https://twitter.com/SPECCHIO_DB

## Slide 22: SPECCHIO over Time – The only constant is change
2002
2006
Bojinski, S., Schaepman, M., Schlaepfer, D. and Itten, K. (2002). "SPECCHIO: a Web-accessible database for the administration and storage of heterogeneous spectral data." Photogrammetry and Remote Sensing 57: 204-211.
Hueni, A., Nieke, J., Schopfer, J., Kneubühler, M. and Itten, K. (2009). "The spectral database SPECCHIO for improved long term usability and data sharing." Computers & Geosciences 35(3): 557-565.
2009
Hueni, A., Malthus, T., Kneubuehler, M., Schaepman, M., 2011. Data Exchange between distributed Spectral Databases. Computers & Geosciences 37, 861–873.
2012
Hueni, A., Chisholm, L., Suarez, L., Ong, C. and Wyatt, M. (2012). Spectral Information System Development for Australia. Geospatial Science Research Symposium. Melbourne, Australia. 1328: 1-11.
V0
V1
V3
2015
V3.2
SPECCHIO Virtual Machine, SPECCHIO API public, Programming Courses
2017
V2
RSL Internal
Online DB
Exchange
More metadata
Generic metadata
V3.3
Spatial database support
2015
V3.2.1
Operational upgrades
Bertschi, S. and Hueni, A. (2017). Applied Spectral Databases - APEX Spectral Ground Control Point Handling. 10th EARSeL SIG Imaging Spectroscopy Workshop. Zurich, CH.